## Slide 1: Early Detection of Alzheimer’s disease: A Review
Ramin Nourizadeh

## Slide 2: Table of Contents
Introduction
EEG
Evaluation Methods
Methods
Conclusion
Future Works
References

## Slide 3: Introduction
AD
Alois Alzheimer
Notes: Alois Alzheimer (1864 –1915) was a German psychiatrist and neuropathologist

## Slide 4: Introduction
Normal
Very Mild Dementia
Mild Dementia
Moderate Dementia
Severe Dementia
Stages Of Disease:
Notes: probability of Aβ positivity of up to 0.75 for patients with MCI and of 0.60 for SCD subjects
approximately 15–20% of MCI patients progressing to AD each year
Very Mild Dementia: Cognitive decline is noticeable but does not interfere with daily activities.
Mild Dementia: Cognitive decline is noticeable and begins to interfere with daily activities.
Moderate Dementia: Cognitive decline is significant and interferes with daily activities such as dressing and bathing.
Severe Dementia

## Slide 5: Introduction
Amyloid-beta (Aβ)
Stages Of Disease:

## Slide 6: Introduction
AD diagnosis methods
Amyloid-beta (Aβ)
  Begins up to 20 years
Clinical Dementia Rating
Notes: درهم‌تنیدگی‌های نوروفیبریلاری** و **پلاک‌های آمیلوئید بتا** دو مورد از شایع‌ترین علائم بیماری آلزایمر هستند.
پلاک‌ها در ارتباط بین سلول‌های عصبی اختلال ایجاد می‌کنند، در حالی که تصور می‌شود گره‌ها باعث اختلال در حمل و نقل مواد مغذی و دیگر مواد ضروری در سلول‌های عصبی می‌شوند

## Slide 7: Introduction
30% of people are misdiagnosed
Mentioning the type of MCI
aMCI (Amnestic MCI) affects the hippocampus and is detectable in MRI while it is not easy for naMCI (Non-amnestic MCI)
naMCI via an EEG-based biomarker can be more valuable
Alzheimer
Notes: MCI همیشه به زوال عقل منجر نمی‌شود، بلکه گاهی اوقات ثابت می‌ماند یا حتی زمانی که فرد به شرایط طبیعی خود بازگشت، علائم آن از بین می‌رود. متخصصان اختلال شناختی خفیف را به دو نوع "aMCI" و "naMCI" تقسیم کردند. نوع اول به اختلالی گفته می‌شود که بر حافظه اثر می‌گذارد، در حالی که نوع دیگر ، توانایی‌های ذهنی را تحت تاثیر قرار می‌دهد. موضوع قابل توجه اینکه aMCI، خطر ابتلا به بیماری آلزایمر را بیشتر از نوع دیگر افزایش می‌دهد.

## Slide 8: Introduction
AD diagnosis methods
Notes: A **SPECT scan** is a type of imaging test that uses a radioactive substance and a special camera to create 3D pictures

## Slide 9: Introduction
AD diagnosis methods
Comparison of the medical techniques
Notes: توموگرافی کامپیوتری انتشار تک فوتون (SPECT)نوعی آزمایش تصویربرداری است که از یک ماده رادیواکتیو و یک دوربین مخصوص برای ایجاد تصاویر سه بعدی از اندام ها، بافت ها و استخوان ها استفاده می کند.

## Slide 10: Introduction
AD diagnosis methods
Medical imaging techniques
  Voxels and features are extracted
EEG is processed in the time and the frequency domains.
MRI, CT, and PET, EEG recording methods provide good temporal resolution

## Slide 11: EEG
Electroencephalography signals (EEG)
  Detecting electrical activity in the brain
Notes: The distances between adjacent electrodes are either 10% or 20% of the total front-back (nasion-inion) or right-left distance of the skull. large interelectrode distance.

## Slide 12: EEG
EEG Disadvantages :
  Noisy raw data
  Low spatial resolution
  Artifacts
    Power line, bad electrode contact and broken electrodes
    Eye movements, muscle activity, and cardiac signals

## Slide 13: EEG
Stages:
  Data acquisition
  Signal denoising
  Feature extraction
  Classification.

## Slide 14: EEG
200 Hz
In a 10-min eye-closed resting state
Participants were required to remain awake during the entire recording
Capture neural events in milliseconds
Spatial resolution is limited by the number of electrodes
Notes: 200 Hz refers to the sampling rate at which electrical activity in the brain is measured . It means that **200 samples per second

## Slide 15: EEG
Recording
Notes: The distances between adjacent electrodes are either 10% or 20% of the total front-back (nasion-inion) or right-left distance of the skull. large interelectrode distance.

## Slide 16: EEG
Recording
Notes: The distances between adjacent electrodes are either 10% or 20% of the total front-back (nasion-inion) or right-left distance of the skull. large interelectrode distance.

## Slide 17: EEG
Recording
Notes: The distances between adjacent electrodes are either 10% or 20% of the total front-back (nasion-inion) or right-left distance of the skull. large interelectrode distance.

## Slide 18: EEG
Recording
10-10 system

## Slide 19: EEG
Recording

## Slide 20: EEG
3D scalp topography of the power of the EEG recording is shown
Recording

## Slide 21: EEG
Processing
AD diagnosis model

## Slide 22: EEG
Filtering and EEG rhythm calculation
Artifact reduction algorithms
Expert supervision
Data reduction
Source localization
Data augmentation
Normalization, and input generating for Deep Neural Network (DNN)
Preprocessing

## Slide 23: EEG
Determining of the window size
Preprocessing
Notes: last procedure in the pre-processing stage is determining of the window size . It should be long enough to be informative about the dynamic of the system and fulfill the processing method. Long processing windows, on the other hand, can increase the computational cost. Therefore, finding a fit window size is an art.

## Slide 24: EEG
Dimension reduction
Preprocessing

## Slide 25: EEG
Delta: has a frequency of 3 Hz or below
Theta: has a frequency of 3.5 to 7.5 Hz
Alpha: has a frequency between 7.5 and 13 Hz
Beta: : has a frequency between 13 and 25 Hz
Preprocessing

## Slide 26: EEG
Processing
Notes: Alzheimer Disease’s (AD) – Healthy Control (HC) Group EEG signals.

## Slide 27: EEG
Pie chart of the percentages of Decision-making approaches
Overview of Studies
Notes: Abbreviations: Support Vector Machine (SVM), K-Nearest Neighbor (KNN), Linear Discriminant Analysis (LDA), Multilayer Perceptron (MLP), Random Forest (RF), Naïve Bayse (NB), Binary Logistic Regression (BLR), Decision Tree (DT)

## Slide 28: EEG
Transformed to the frequency domain using
  Fourier methodology such as Fast Fourier Transform (FFT)
  Welch Power Spectral Density (PSD) analysis
Transformed to the time-frequency domain using decomposition such as
  Discrete Wavelet Transform (DWT)
  Empirical Mode Decomposition (EMD)
Right choice of the features removed up to 82% of the EEG spectral features and increased the accuracy of the classifier more than 17%
Feature Extraction
Notes: Almost all the studies have employed band pass filter or discrete wavelet transform (DWT) to remove some artifacts that lie in a limited frequency band or specific artifacts
right choice of the feature selection method removed up to 82% of the EEG spectral features and increased the accuracy of the classifier more than 17%

## Slide 29: EEG
Event Related Potentials (ERP)
  ERP are electric potentials elicited in the brain as a response to an auditory or visual stimulus.
Complexity
  Lower complexity and irregularity compared to HC
Time domain features

## Slide 30: EEG
Coherence
  This metric evaluates the synchrony between two signals
  Increase of coherence in delta and theta rhythms, and a decrease in alpha and beta rhythms in MCI and AD
Relative power
  This metric quantifies the proportion of power that is contained in an EEG sub band, compared to the total power of the signal.
  Relative power in the fast rhythms (alpha and beta) decreases, while the relative power in the slow rhythms (delta and theta) increases.
Frequency domain analysis
Notes: انسجام این متریک همگامی بین دو سیگنال را ارزیابی می کند. انسجام به کوواریانس نرمال شده دو سیگنال در حوزه طیفی اشاره دارد. در ادبیات، نویسندگان افزایش انسجام در ریتم‌های دلتا و تتا و کاهش ریتم‌های آلفا و بتا را در MCI و AD گزارش کرده‌اند. قدرت نسبی این متریک نسبت توان موجود در یک زیر باند EEG را در مقایسه با توان کل سیگنال کمیت می کند. این بدان معناست که قدرت نسبی در ریتم های تند (آلفا و بتا) کاهش می یابد، در حالی که قدرت نسبی در ریتم های آهسته (دلتا و تتا) افزایش می یابد.

## Slide 31: EEG
88 subjects
  36 Alzheimer’s patients
  23 frontotemporal dementia patients
  29 healthy age-matched subjects
Datasets
Miltiadous, A.; Tzimourta, K.D.; Afrantou, T.; Ioannidis, P.; Grigoriadis, N.; Tsalikakis, D.G.; Angelidis, P.; Tsipouras, M.G.; Glavas, E.; Giannakeas, N.; et al. A Dataset of Scalp EEG Recordings of Alzheimer’s Disease, Frontotemporal Dementia and Healthy Subjects from Routine EEG. Data 2023, 8, 95. https://doi.org/10.3390/data8060095
Notes: FTD is characterized by changes in personality, behavior, and language.FTD, on the other hand, predominantly affects the frontal and temporal lobes of the brain. It is characterized by changes in personality, behavior, and language. The disease can cause people to become socially inappropriate, impulsive, or emotionally indifferent.

## Slide 32: EEG
27 subjects
  16 normal
  11 MCI
Datasets
M. Kashefpoor, H. Rabbani, M. Barekatain, "Supervised dictionary learning of EEG signals for mild cognitive impairment diagnosis", Biomedical Signal Processing & Control, vol. 53, pp. 101559, 2019.

## Slide 33: Evaluation Methods
K-fold
    Dataset is randomly split into k equal-sized folds
    Each fold is then used as a test set once, while the remaining k-1 folds are used as the training set
    This process is repeated k times, with each fold serving as the test set exactly once.

## Slide 34: Evaluation Methods
LOSO CV (Leave-One-Out Cross-Validation) **
  Split the dataset into training and testing sets, using all but one observation as part of the training set.
  Build the model using only data from the training set.
  Use the model to predict the response value of the one observation left out of the model and calculate the mean squared error (MSE).
  Repeat the process for each observation in the dataset, leaving out a different observation from the training set each time.
  Calculate the test MSE to be the average of all of the test MSEs.
Notes: A model is then built using only data from the training set, and the model is used to predict the response value of the one observation left out of the model. This process is repeated n times

## Slide 35: Methods
Deep learning techniques in AD assessment:
  Convolutional neural network (CNN)
  MC-DCNN (Multi-Channel Deep Convolutional Neural Network )
  Stacked autoencoder (SAE)
  Spatial Temporal Convolutional Networks (ST-CNN)
  Transformers

## Slide 36: Methods
890 participants
  189 MCI
  330 AD
  125 other dementias
  246 Healthy
Overview
Jiao B, Li R, Zhou H, Qing K, Liu H, Pan H, et al. Neural biomarker diagnosis and prediction to mild cognitive impairment and Alzheimer’s disease using EEG technology. Alzheimer's Research & Therapy. 2023;15(1):32.
Notes: Datasets are available from the corresponding author upon reasonable request

## Slide 37: Methods
Fouad IA, El-Zahraa M. Labib F. Identification of Alzheimer’s disease from central lobe EEG signals utilizing machine learning and residual neural network. Biomedical Signal Processing and Control. 2023;86.
Use three central lobe electrodes
Dataset
  7 MCI
  59 AD
  102 NC
Performance is 96.55%
Notes: This EEG dataset is available as open source.

## Slide 38: Methods
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
Using a Dual-Input Convolution Encoder Network
Public dataset from Department of Neurology of AHEPA General University Hospital of Thessaloniki
  36 AD
  23 Frontotemporal dementia (FTD)
  29 CN

## Slide 39: Methods
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
Extract two biomarkers
  Relative Band Power (RBP): increase in Theta/Alpha ratio in AD patients
  Spectral Coherence Connectivity (SCC): decreased synchronization likelihood in AD patients
Express them in image-like representations (3d matrixes)
Notes: First, each recording was divided into 30-second time windows with 15 seconds overlap to create the pool of EEG signals that will be used for the classification task. Next, the following two features have been extracted

## Slide 40: Methods
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
Preprocessing pipeline
  Butterworth band-pass filter 0.5-45 Hz
  Re-referenced to A1-A2
  Automatic artifact reject method
    ASR
Notes: First, each recording was divided into 30-second time windows with 15 seconds overlap to create the pool of EEG signals that will be used for the classification task. Next, the following two features have been extracted

## Slide 41: Methods
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
Fed in 2 parallel Convolution blocks
Accuracy of 83.28% LOSO validation

## Slide 42: Methods
Nour M, Senturk U, Polat K. A novel hybrid model in the diagnosis and classification of Alzheimer's disease using EEG signals: Deep ensemble learning (DEL) approach. Biomedical Signal Processing and Control. 2024;89.
Two datasets were used
Divides EEG signals into 5 frequency bands with a Butterworth band-pass filter
Signals recorded as 8 s in the datasets were segmented into 1 s epochs
An epoch was converted into a 2D array of 128x19. A total of 1120 epochs consist of two datasets combined
Then, EEG signals for each frequency band (delta, theta, alpha, beta, and gamma) were segmented into 1 s epochs (128x19 2D array) and given as input to ensemble learning
Accuracy of 97.9%
Notes: We can send the datasets at the request of the authors

## Slide 43: Methods
Nour M, Senturk U, Polat K. A novel hybrid model in the diagnosis and classification of Alzheimer's disease using EEG signals: Deep ensemble learning (DEL) approach. Biomedical Signal Processing and Control. 2024;89.
The proposed Deep Ensemble Learning

## Slide 44: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
Transformers
  Higher ability to deal with long-range dependencies
  Recognize patterns in sequences of data
  More interpretable decision-making processes
  Recent efforts in exploring their applications on timeseries data, such as EEG or electromyography signals are showing interesting results

## Slide 45: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
Best performances
  delta dataset
  Performance of 0.807
Performance with a minimum features is higher than 0.74
Adding available 61 EEG channels, instead of a cluster of 19 channels, not only did not improve the performances of the model
Notes: Five different datasets were created by extracting
  delta, theta, alpha, beta and delta-to-theta frequency bands using bandpass filters

## Slide 46: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
Workflow of the proposed method

## Slide 47: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
EEG epoch classification pipeline
Notes: Each EEG segment of C = 19 channels and D = 5120 datapoints is used
uses a convolutional layer to compress the signal, extract slices and embed the information. k = 31 is the size of the kernel, emb = 6 is the embeddings’ dimension and CLS is the classification token prepended to the input. Attention mechanism is then applied on the temporal domain and, after global average pooling, a linear layer is used to classify the input EEG epoch

## Slide 48: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
Proposed transformer architecture
Notes: CLS is the classification token, h = 3 is the number of heads used by multi-head attention and Depth = 2 indicates the number of times the transformer encoder block is repeated. A legend for uncaptioned blocks is provided on the bottom right corner

## Slide 49: Methods
Morabito, F. C., et al. (2017). "Deep Learning Representation from Electroencephalography of Early-Stage Creutzfeldt-Jakob Disease and Features for Differentiation from Rapidly Progressive Dementia." Int J Neural Syst 27(2): 1650039.
The 19-channel EEG recording is partitioned into N nonoverlapping 5s windows
For each EEG epoch, and for every EEG channel a time-frequency representation (TFR) is computed. The TFRs are averaged over epochs resulting in 19 averaged TFRs (one per channel). Each averaged TFR is subdivided into three sub bands, and then, the mean (μ), the standard deviation (σ), and the skewness (v) are estimated both for the sub bands and for the whole TFR.
The first autoencoder compresses the input representation in 40 parameters . The second autoencoder compresses the 40 learned features in 20 higher-level paraments
A classifier with a single hidden layer of 10 neurons is trained

## Slide 50: Methods
Morabito, F. C., et al. (2017). "Deep Learning Representation from Electroencephalography of Early-Stage Creutzfeldt-Jakob Disease and Features for Differentiation from Rapidly Progressive Dementia." Int J Neural Syst 27(2): 1650039.

## Slide 51: Methods
Aljalal, M., et al. (2024). "Mild cognitive impairment detection with optimally selected EEG channels based on variational mode decomposition and supervised machine learning." Biomedical Signal Processing and Control 87.
The study analyzed a total of eight EEG features obtained from 21 channels.
Used two public datasets that are both available

## Slide 52: Methods
Aljalal, M., et al. (2024). "Mild cognitive impairment detection with optimally selected EEG channels based on variational mode decomposition and supervised machine learning." Biomedical Signal Processing and Control 87.
Overview

## Slide 53: Methods
Aljalal, M., et al. (2024). "Mild cognitive impairment detection with optimally selected EEG channels based on variational mode decomposition and supervised machine learning." Biomedical Signal Processing and Control 87.
Example of feature extraction from a 10 sec segment using VMD and Shannon entropy.
Notes: Variational Mode Decomposition (VMD) is a signal processing technique that decomposes a signal into a finite number of intrinsic mode functions

## Slide 54: Methods
Aljalal, M., et al. (2024). "Mild cognitive impairment detection with optimally selected EEG channels based on variational mode decomposition and supervised machine learning." Biomedical Signal Processing and Control 87.
Example of channel representation in a chromosome

## Slide 55: Methods
Aljalal, M., et al. (2024). "Mild cognitive impairment detection with optimally selected EEG channels based on variational mode decomposition and supervised machine learning." Biomedical Signal Processing and Control 87.
EEG channel selection using NSGA for MCI classification
Accuracy using all 19 EEG channels is 99.51%

## Slide 56: Methods
Siddhad, G., et al. (2024). "Efficacy of transformer networks for classification of EEG data." Biomedical Signal Processing and Control 87: 105488.
EEG with a window size of 0.25 s
Independent component analysis (ICA) is applied
Bad channels are manually removed
Accuracies of 94.68% were achieved
This proves the effectiveness of the transformers for processing raw EEG data
  Can reduce the need for feature extraction in EEG .

## Slide 57: Methods
Siddhad, G., et al. (2024). "Efficacy of transformer networks for classification of EEG data." Biomedical Signal Processing and Control 87: 105488.
Stack of 4 encoders are used in the proposed method

## Slide 58: Methods
Siddhad, G., et al. (2024). "Efficacy of transformer networks for classification of EEG data." Biomedical Signal Processing and Control 87: 105488.
Proposed architecture for Age and Gender dataset

## Slide 59: Methods
Siddhad, G., et al. (2024). "Efficacy of transformer networks for classification of EEG data." Biomedical Signal Processing and Control 87: 105488.
Proposed architecture for STEW dataset

## Slide 60: Methods
Modir, A., et al. (2023). "A systematic review and methodological analysis of EEG-based biomarkers of Alzheimer's disease." Measurement 220.
Multimodal neuroimaging system and their aim in AD assessment
Notes: fNIR and fMRI are both neuroimaging techniques that are used to study the brain. fNIR stands for functional near-infrared spectroscopy. Both techniques are used to measure changes in blood flow in the brain, but they differ in how they do so. fMRI uses a strong magnetic field and radio waves to measure changes in blood oxygenation, while fNIR uses near-infrared light to measure changes in blood oxygenation

## Slide 61: Methods
Tucci, F., et al. (2023). "What a single electroencephalographic (EEG) channel can tell us about Alzheimer's disease patients with mild cognitive impairment." Alzheimer's & Dementia 19(S2): e062375.
Monitoring of AD progression in large populations with few electrodes in low-cost devices
Data acquired in hospital settings (10-20 montage) from 75 ADMCI participants and 70 age-, education-, and sex-matched normal elderly controls (Nold) were available in an Italian-Turkish archive (www.pdwaves.eu)
Standard spectral Fast Fourier Transform (FFT) analysis of rsEEG data for individual delta, theta, and alpha frequency bands was computed from 6 monopolar scalp electrodes to derive bipolar C3-P3, C4-P4,O1 and O2 markers

## Slide 62: Methods
Tucci, F., et al. (2023). "What a single electroencephalographic (EEG) channel can tell us about Alzheimer's disease patients with mild cognitive impairment." Alzheimer's & Dementia 19(S2): e062375.

## Slide 63: Methods
Tucci, F., et al. (2023). "What a single electroencephalographic (EEG) channel can tell us about Alzheimer's disease patients with mild cognitive impairment." Alzheimer's & Dementia 19(S2): e062375.
The ADMCI group showed increased delta and decreased alpha power density
Best classification accuracy between the ADMCI and Nold individuals reached 81% using Alpha2/Theta power density computed at the C3-P3 bipolar channel..

## Slide 64: Methods
Tucci, F., et al. (2023). "What a single electroencephalographic (EEG) channel can tell us about Alzheimer's disease patients with mild cognitive impairment." Alzheimer's & Dementia 19(S2): e062375.
Demographic and clinical data in Nold and ADMCI
To evaluate the study hypotheses, clinical, neuropsychological, anthropometric, genetic, cerebrospinal fluid (CSF), MRI, and rsEEG data in 70 Nold and 75 ADMCI subjects from an international archive were used in the present study

## Slide 65: Methods
Fouladi, S., et al. (2022). "Efficient Deep Neural Networks for Classification of Alzheimer’s Disease and Mild Cognitive Impairment from Scalp EEG Recordings." Cognitive Computation 14(4): 1247-1268.
Two different deep learning (DL) architectures
  Modified convolutional (CNN) with accuracy 92%
  Convolutional autoencoder (Conv-AE) neural networks (NNs) with accuracy 89 %

## Slide 66: Methods
Fouladi, S., et al. (2022). "Efficient Deep Neural Networks for Classification of Alzheimer’s Disease and Mild Cognitive Impairment from Scalp EEG Recordings." Cognitive Computation 14(4): 1247-1268.
19-channel
90 subjects
  37 AD
  37 MCI
  16 HC
Recorded in 5-m

## Slide 67: Conclusion

## Slide 68: Conclusion
Need to provide an open-access and proper EEG database
Almost all the researchers applied their own database and it makes the comparison among the performance of studies very challenging
95% of the studies were conducted with fewer than 100 participants
Public medical imaging databases like ADNI or OASIS is a common practice in AD

## Slide 69: Future Works
Longitudinal studies
Other neurological disorders,
  Parkinson’s
  epilepsy
  stroke
Notes: Longitudinal studies to assess whether EEG biomarkers can be used to trace the progress trajectory of AD or evaluate the efficacy of pharmacological/therapeutic interventions for AD patients.

## Slide 70: Future Works
In transformer model
  Add spatial attention module on the EEG channels
Study of new features that support the early detection of AD

## Slide 71: Future Works
Multi modal EEG-based biomarker
  Combined with neuroimaging techniques
  Novel deep neural network architecture
    Explains its reason for each output prediction

## Slide 72: References
Jiao B, Li R, Zhou H, Qing K, Liu H, Pan H, et al. Neural biomarker diagnosis and prediction to mild cognitive impairment and Alzheimer’s disease using EEG technology. Alzheimer's Research & Therapy. 2023;15(1):32.
Fouad IA, El-Zahraa M. Labib F. Identification of Alzheimer’s disease from central lobe EEG signals utilizing machine learning and residual neural network. Biomedical Signal Processing and Control. 2023;86.
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
Nour M, Senturk U, Polat K. A novel hybrid model in the diagnosis and classification of Alzheimer's disease using EEG signals: Deep ensemble learning (DEL) approach. Biomedical Signal Processing and Control. 2024;89.
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.

## Slide 73: References
Perez-Valero E, Lopez-Gordo MA, Morillas C, Pelayo F, Vaquero-Blasco MA. A Review of Automated Techniques for Assisting the Early Detection of Alzheimer’s Disease with a Focus on EEG. Journal of Alzheimer's Disease. 2021;80(4):1363-76.
Jiao B, Li R, Zhou H, Qing K, Liu H, Pan H, et al. Neural biomarker diagnosis and prediction to mild cognitive impairment and Alzheimer’s disease using EEG technology. Alzheimer's Research & Therapy. 2023;15(1):32.
Morabito, F. C., et al. (2017). "Deep Learning Representation from Electroencephalography of Early-Stage Creutzfeldt-Jakob Disease and Features for Differentiation from Rapidly Progressive Dementia." Int J Neural Syst 27(2): 1650039.
Aljalal, M., et al. (2024). "Mild cognitive impairment detection with optimally selected EEG channels based on variational mode decomposition and supervised machine learning." Biomedical Signal Processing and Control 87.
Siddhad, G., et al. (2024). "Efficacy of transformer networks for classification of EEG data." Biomedical Signal Processing and Control 87: 105488.

## Slide 74: References
Saleh, H., et al. (2023). "Computer aided progression detection model based on optimized deep LSTM ensemble model and the fusion of multivariate time series data." Scientific Reports 13(1): 16336.
Modir, A., et al. (2023). "A systematic review and methodological analysis of EEG-based biomarkers of Alzheimer's disease." Measurement 220.
Fouladi, S., et al. (2022). "Efficient Deep Neural Networks for Classification of Alzheimer’s Disease and Mild Cognitive Impairment from Scalp EEG Recordings." Cognitive Computation 14(4): 1247-1268.
Tucci, F., et al. (2023). "What a single electroencephalographic (EEG) channel can tell us about Alzheimer's disease patients with mild cognitive impairment." Alzheimer's & Dementia 19(S2): e062375.

## Slide 75: Thank You