## Slide 1: Early Detection of Alzheimer’s disease
Ramin Nourizadeh

## Slide 2: Table of Contents
Introduction to Protein
Recent advances in protein design,
  shifting from a physical-based function paradigm to one that uses deep learning
Discuss challenges to the design of marketable proteins with controllable properties.

## Slide 3: Introduction
AD Stages
it has been established that SCD can occur at late stages of preclinical AD, before MCI is reached. This phase can be also referred to as pre-MCI or preprodromal AD.
probability of Aβ positivity of up to 0.75 for patients with MCI and of 0.60 for SCD subjects

## Slide 4: Introduction
AD diagnosis methods
biological markers, such as amyloid-beta (Aβ) protein accumulation, which is distinctive in AD, may be found in the brain up to 20 years before the stage of dementia

## Slide 5: Introduction
AD diagnosis methods

## Slide 6: Introduction
AD diagnosis methods
Comparison of the medical techniques described in the Introduction section

## Slide 7: Introduction
AD diagnosis methods
medical imaging techniques
  images are typically segmented into voxels and features are extracted
EEG is processed in the time and the frequency domains.

## Slide 8: Introduction
AD diagnosis methods
The EEG electrode placement was standardized in a 10–20 system, which is a method to describe the location of electrodes over the scalp. This system is based on the relationship between the location of the electrode and underlying brain lobes. The distances between adjacent electrodes are either 10% or 20% of the total front-back (nasion-inion) or right-left distance of the skull. large interelectrode distance.

## Slide 9: Introduction
More than 95% of the studies that focused on EEG-based classification were conducted with fewer than 100 participants.
public medical imaging databases like ADNI or OASIS is a common practice in AD literatures
in EEG studies, due to the high accessibility of this technique, researchers generally acquire their own data
Dataset

## Slide 10: Introduction
Clinical-demographic characteristics of population
Dataset

## Slide 11: Introduction
EEG changes related to AD progression into four main categories:
  slowing,
  complexity reduction,
  synchronization decrement and
  neuromodulatory deficit
These effects include EEG slowing, loss of synchronization, and complexity reduction
EEG

## Slide 12: Introduction
Electroencephalography signals (EEG) are a method of detecting electrical activity in the brain
changes can include increased slow brainwaves (delta and theta waves) [20] and decreased faster waves (alpha and beta waves)
an increased Theta/Alpha ratio has also been reported for subjects with mild AD
can be used to monitor changes in brain activity associated with the progression of the disease and help doctors adjust treatments and make better decisions.
EEG

## Slide 13: Introduction
EEG signal was recorded at 200 Hz
In a 10-min eye-closed resting state
Participants were required to remain awake during the entire recording
Standard 16-channels montage was utilized according to the 10–20 International System.
EEG Recording

## Slide 14: Introduction
With a standard 10–20 system, the average intersensor distance is 7cm. Achieving a 1 to 2cm sampling density would require 500 EEG channels distributed uniformly over the scalp. High-density-EEG (HD-EEG) offers a high temporal resolution, typical of EEG, in conjunction with a high spatial resolution (Fig. 8). HD-EEG with 256 channels provides adequate approximate spatial sampling [23,24]. An example of high-density EEG recording is shown
High-density 256 channels EEG recording system
EEG Recording

## Slide 15: Introduction
A 30 s sample of high-density 256 channels EEG recording
EEG Recording

## Slide 16: Introduction
3D scalp topography of the power of the EEG recording is shown
standard 19 channels
EEG Recording

## Slide 17: Introduction
Patients with MCI and AD generally showed decreased alpha/beta power and increased theta/delta power in a broad range of brain regions such as frontal, temporal, parietal, and occipital areas
Alzheimer

## Slide 18: Introduction
stated that 30% of people are misdiagnosed
Alzheimer

## Slide 19: Introduction
EEG signal was recorded at 200 Hz
In a 10-min eye-closed resting state
Participants were required to remain awake during the entire recording
Standard 16-channels montage was utilized according to the 10–20 International System.
EEG can capture neural events in the order of milliseconds , but its spatial resolution is limited by the number of electrodes used to record the electrical activity of the brain.
EEG is noisy and nonstationary multivariate time series
EEG Recording

## Slide 20: Introduction
The EEG electrode placement was standardized in a 10–20 system, which is a method to describe the location of electrodes over the scalp. This system is based on the relationship between the location of the electrode and underlying brain lobes. The distances between adjacent electrodes are either 10% or 20% of the total front-back (nasion-inion) or right-left distance of the skull. large interelectrode distance.
EEG Recording

## Slide 21: Introduction
A wavelet transform reveals important information in a signal’s time–frequency domain through analysis of frequency components.
EEG Processing

## Slide 22: Introduction
Considering the complexity of EEG signals, classifier models should be reduced to more straightforward features that can be calculated.
EEG Processing

## Slide 23: Introduction
four stages:
  data acquisition,
  signal denoising,
  feature extraction,
  classification.
EEG Processing

## Slide 24: Introduction
The five frequency bands of B were defined as:
  Delta: 0.5 – 4 Hz
  Theta: 4 – 8 Hz
  Alpha: 8 – 13 Hz
  Beta: 13-25 Hz
  Gamma: 25-45 Hz
EEG Processing

## Slide 25: Introduction
EEG Processing
Block diagram AD diagnosis DEL model

## Slide 26: Introduction
EEG Processing
Alzheimer Disease’s (AD) – Healthy Control (HC) Group EEG signals.

## Slide 27: Introduction
EEG Processing
Sample EEG recordings of subject 1. (top) 5 s window of raw EEG signal. (bottom) Same window after preprocessing.

## Slide 28: Introduction
decompose it into other frequency bands, such as delta, theta, alpha, beta, and gamma
Each frequency band represents a diverse range of electrical activity in the brain
  delta band :0.5-4 Hz, deep sleep and the maintenance of bodily functions
  alpha band:8-13 Hz, attentional processes and relaxation
EEG Feature Extraction

## Slide 29: Introduction
usually transformed to the frequency domain using
  Fourier methodology such as Fast Fourier Transform (FFT)
  Welch Power Spectral Density (PSD) analysis
transformed to the time-frequency domain using decomposition such as
  Discrete Wavelet Transform (DWT)
  Empirical Mode Decomposition (EMD)
EEG Feature Extraction

## Slide 30: Introduction
After the transformation or analysis of EEG data with one of the following features are usually extracted to be fed to a Machine Learning framework for automatic detection, prediction, severity assessment, or evaluation of the given EEG task
  abovementioned methodologies,
  band power,
  entropy,
  fractal dimension, or
  statistical
EEG Feature Extraction

## Slide 31: Introduction
right choice of the feature selection method removed up to 82% of the EEG spectral features and increased the accuracy of the classifier more than 17%
EEG Feature Extraction

## Slide 32: Introduction
Event-related potentials (ERP)
  ERP are electric potentials elicited in the brain as a response to an auditory or visual stimulus.
Complexity
  Brain activity in MCI and AD patients has lower complexity and irregularity compared to HC
EEG time domain features for AD detection

## Slide 33: Introduction
Coherence
  This metric evaluates the synchrony between two signals. More formally, coherence refers to the normalized covariance of two signals in the spectral domain. In literature, authors have reported an increase of coherence in delta and theta rhythms, and a decrease in alpha and beta rhythms in MCI and AD
Relative power
  This metric quantifies the proportion of power that is contained in an EEG sub band, compared to the total power of the signal. This means that the relative power in the fast rhythms (alpha and beta) decreases, while the relative power in the slow rhythms (delta and theta) increases.
EEG Frequency domain analysis for AD detection

## Slide 34: Introduction
Fourier transform
  This transform is used to decompose a time signal into a sum of sines and cosines of different frequencies and infinite length. spectral content of the EEG cannot be tracked by the Fourier transform, as the sines and cosines used in this transform are infinite length. Conversely, the wavelet transform represents a suitable alternative to address this issue.
Amplitude modulation
  This methodology combines temporal and frequency analysis.
EEG Frequency domain analysis for AD detection

## Slide 35: Introduction
LOSO CV
  most straightforward and clear model validation approach for AD classification. LOSO CV is the most suitable validation Amplitude modulation
performance evaluation methods

## Slide 36: Methods
A total of 890 participants, including 189 patients with MCI, 330 patients with AD, 125 patients with other dementias and 246
Datasets are available from the corresponding author upon reasonable request
Overview
Jiao B, Li R, Zhou H, Qing K, Liu H, Pan H, et al. Neural biomarker diagnosis and prediction to mild cognitive impairment and Alzheimer’s disease using EEG technology. Alzheimer's Research & Therapy. 2023;15(1):32.

## Slide 37: Methods
Fouad IA, El-Zahraa M. Labib F. Identification of Alzheimer’s disease from central lobe EEG signals utilizing machine learning and residual neural network. Biomedical Signal Processing and Control. 2023;86.
Three central lobe electrodes
This EEG dataset is available as open source.
The dataset contains 7 MCI, 59 AD, and 102 NC subjects
Highest performance of 96.55%

## Slide 38: Methods
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
classification using a Dual-Input Convolution Encoder Network
: Recordings of 36 AD, 23 Frontotemporal dementia (FTD), and 29 age-matched healthy individuals (CN) were used
accuracy of 83.28% in the AD-CN problem using Leave-One-Subject-Out validation

## Slide 39: Methods
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
First, each recording was divided into 30-second time windows with 15 seconds overlap to create the pool of EEG signals that will be used for the classification task. Next, the following two features have been extracted

## Slide 40: Methods
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
extract two of the most promising biomarkers
  Relative Band Power (RBP): increase in Theta/Alpha ratio in AD patients
  Spectral Coherence Connectivity (SCC): decreased synchronization likelihood in AD patients

## Slide 41: Methods
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
express them in image-like representations (3d matrixes)
fed in 2 parallel Convolution blocks

## Slide 42: Methods
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
recordings from 88 participants
  from Department of Neurology of AHEPA General University Hospital of Thessaloniki.
  36 (13 males) of them were diagnosed with Alzheimer’s disease (AD group), 23 (14 males) were diagnosed with Frontotemporal Dementia (FTD group), and 29 (11 males) were healthy subjects (CN group)

## Slide 43: Methods
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
The preprocessing pipeline of the EEG signals is as follows. First, a Butterworth band-pass filter 0.5-45 Hz was applied, and the signals were re-referenced to A1-A2. Then, the ASR routine [12] which is an automatic artifact reject method that can remove transient or large-amplitude artifacts

## Slide 44: Methods
Miltiadous A, Gionanidis E, Tzimourta KD, Giannakeas N, Tzallas AT. DICE-Net: A Novel Convolution-Transformer Architecture for Alzheimer Detection in EEG Signals. IEEE Access. 2023;11:71840-58.
We made the dataset publicly available

## Slide 45: Methods
Nour M, Senturk U, Polat K. A novel hybrid model in the diagnosis and classification of Alzheimer's disease using EEG signals: Deep ensemble learning (DEL) approach. Biomedical Signal Processing and Control. 2024;89.
This paper divides EEG signals into 5 frequency bands with a Butterworth band-pass filter. EEG signals recorded as 8 s in the datasets were segmented into 1 s epochs. An epoch was converted into a 2D array of 128x19. A total of 1120 epochs consist of two datasets combined. Then, EEG signals for each frequency band (delta, theta, alpha, beta, and gamma) were segmented into 1 s epochs (128x19 2D array) and given as input to ensemble learning
With 5 cross-fold training, the average accuracy of the DEL model reached 97.9% ± 1.1%.

## Slide 46: Methods
Nour M, Senturk U, Polat K. A novel hybrid model in the diagnosis and classification of Alzheimer's disease using EEG signals: Deep ensemble learning (DEL) approach. Biomedical Signal Processing and Control. 2024;89.
Two datasets were used
We can send the datasets at the request of the authors

## Slide 47: Methods
Nour M, Senturk U, Polat K. A novel hybrid model in the diagnosis and classification of Alzheimer's disease using EEG signals: Deep ensemble learning (DEL) approach. Biomedical Signal Processing and Control. 2024;89.
. The proposed Deep Ensemble Learning (DEL) Models for AD-HC Classification

## Slide 48: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
Five different datasets were created by extracting delta, theta, alpha, beta and delta-to-theta frequency bands using bandpass filters.
delta dataset allowed our model to achieve the best performances for the discrimination of SCD and MCI, reaching an Area Under the ROC Curve (AUC) of 0.807
esults for the HC vs SCD vs MCI classification were obtained on alpha and theta with a micro-AUC higher than 0.74.

## Slide 49: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
Firstly, raw EEG signals are preprocessed
19 channels are selected and 4 frequency bands (δ, θ, α and β) are extracted
obtaining four distinct datasets and a fifth one using the δ-to-β range.
perform both two- and three-class classifications of epochs through LOSOCV.
Finally, a majority voting approach is used to label each subject in the test set either as HC, SCD or MCI based on the class assigned to its epochs.

## Slide 50: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
transformers
  higher ability to deal with long-range dependencies
  recognize patterns in sequences of data
  more interpretable decision-making processes
  recent efforts in exploring their applications on timeseries data, such as EEG or electromyography signals,are showing interesting results

## Slide 51: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
The electrodes were placed according to the 10–10 montage system and electrode-skin impedance was set below 5 kΩ. Subjects were sat in a reclined chair for approximately 20 min.
A cluster of 19 channels, namely Fp1, Fp2, F7, F3, Fz, F4, F8, T3, C3, Cz, C4, T4, T5, P3, Pz, P4, T6, O1, O2, was then selected. Since these channels evenly cover the scalp area, this EEG pattern is the most employed in the literature for similar studies [56] and has been proven to ensure sufficient quality along with possible comparison with previous rsEEG findings of other projects

## Slide 52: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
adding more spatial details by using all available 61 EEG channels, instead of a cluster of 19 channels, not only did not improve the performances of the model

## Slide 53: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
Workflow of the proposed method

## Slide 54: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
EEG epoch classification pipeline. Each EEG segment of C = 19 channels and D = 5120 datapoints is used as input to our model, which uses a convolutional layer to compress the signal, extract slices and embed the information. k = 31 is the size of the kernel, emb = 6 is the embeddings’ dimension and CLS is the classification token prepended to the input. Attention mechanism is then applied on the temporal domain and, after global average pooling, a linear layer is used to classify the input EEG epoch

## Slide 55: Methods
Sibilano E, Brunetti A, Buongiorno D, Lassi M, Grippo A, Bessi V, et al. An attention-based deep learning approach for the classification of subjective cognitive decline and mild cognitive impairment using resting-state EEG. Journal of Neural Engineering. 2023;20(1):016048.
Proposed transformer architecture. CLS is the classification token, h = 3 is the number of heads used by multi-head attention and Depth = 2 indicates the number of times the transformer encoder block is repeated. A legend for uncaptioned blocks is provided on the bottom right corner

## Slide 56: Methods
Morabito, F. C., et al. (2017). "Deep Learning Representation from Electroencephalography of Early-Stage Creutzfeldt-Jakob Disease and Features for Differentiation from Rapidly Progressive Dementia." Int J Neural Syst 27(2): 1650039.
(A) The 19-channel EEG recording is partitioned into N nonoverlapping 5s windows. (B) For each EEG epoch, and for every EEG channel a time-frequency representation (TFR) is computed. The TFRs are averaged over epochs resulting in 19 averaged TFRs (one per channel). Each averaged TFR is subdivided into three subbands, and then, the mean (μ), the standard deviation (σ), and the skewness (v) are estimated both for the subbands and for the whole TFR. Therefore, 1219¼228 engineered features are extracted and are used to train 2 stacked autoencoders (UL). (C) The first autoencoder (AE1, 228:40:228) compresses the input representation in 40 parameters (h1). The second autoencoder (AE2, 40:20:40) compresses the 40 learned features in 20 higher-level paraments (h2). Finally, a classifier with a single hidden layer (h3) of 10 neurons is trained (SL)

## Slide 57: Future Works
Evaluate the effectiveness of EEG techniques in diagnosing different types of dementias
Longitudinal studies to assess whether EEG biomarkers can be used to trace the progress trajectory of AD or evaluate the efficacy of pharmacological/therapeutic interventions for AD patients.
the model’s accuracy can be further improved using regularization techniques
interpretability

## Slide 58: Future Works
other neurological disorders, such as Parkinson’s, epilepsy, and stroke, to diagnose and classify various diseases
In transformer model improvement of the proposed model, which could include the application of a spatial attention module on the EEG channels, is worth exploring
study of new features that support the early detection of AD

## Slide 59: References
Molecular Biology, Not Only for Bioinformaticians. Istrail, 2013
From sequence to function through structure: Deep learning for protein design
NoeliaFerruz -2023

## Slide 60: Thank You